## Slide 1
AI-Based Approaches for
Drunk Driving Detection
In-Vehicle and Out-Vehicle Techniques, Challenges, and Future Directions
Alsulieman et al. | IEEE Open Journal of the Computer Society | 2026

## Slide 2
AGENDA
Presentation Overview
01
Problem & Motivation
Why AI detection is critical for road safety
02
Key Contributions
Taxonomy, modalities, and comparative analysis
03
In-Vehicle Techniques
Breath, image, iris, biological, behavior & audio
04
Out-Vehicle Techniques
Roadside cameras, drones & external monitoring
05
Challenges & Limitations
Sensing reliability, privacy, and robustness
06
Future Directions
Multimodal fusion and scalable deployment

## Slide 3
THE PROBLEM
Drunk Driving: A Critical Public Safety Challenge
~34%
of U.S. traffic deaths
linked to alcohol
Reactive
Traditional methods
(breathalyzers, tests)
High
Incidence remains
despite strict laws
Why Traditional Methods Fall Short
Breathalyzers and sobriety tests are typically used after an incident or during routine checks
In-vehicle sensor systems can be intrusive, costly, and raise privacy concerns
Without out-vehicle monitoring, authorities cannot identify impaired drivers preventively
Alcohol impairs reaction time, decision-making, coordination, and visual processing

## Slide 4
CONTRIBUTIONS
What This Survey Adds
Deployment-Oriented Taxonomy
Organizes systems into in-vehicle and out-vehicle approaches for clearer real-world implementation perspective.
Expanded Sensing Modalities
Adds audio-based detection alongside breath, image, iris, physiological, and driving behavior analysis.
Structured Comparative Analysis
Summary tables covering sensing modalities, datasets, strengths, limitations, and system responses.
Open Challenges & Future Paths
Identifies issues in reliability, robustness, privacy, and feasibility with research directions.

## Slide 5
TAXONOMY
In-Vehicle vs Out-Vehicle Detection
IN-VEHICLE
Breath Sensors
MQ-3, electrochemical, ignition lock
Image Recognition
Facial features, thermal, CNNs
Iris Recognition
Blink, pupil, eye closure (EAR)
Biological Sensors
Heart rate, rPPG, skin temp
Driving Behavior
Steering, speed, acceleration
Audio Analysis
Speech features, MFCC, CNN
OUT-VEHICLE
Driving Behavior Analysis
UAV/drone trajectories, V2X, velocity
Image Recognition
Roadside cameras, NIR, cell-phone/seatbelt
Infrastructure Sensors
Traffic cams, radar, large-scale monitoring
Enforcement Focus
Passive monitoring, authority alerts

## Slide 6
IN-VEHICLE TECHNIQUES
Breath, Image & Iris Recognition
Breath Sensors
• MQ-3 / electrochemical sensors
• Ignition interlock & alerts
• Helmet-integrated systems
• IoT + GPS + cloud alerts
• Strength: Direct BAC measure
• Limitation: Placement & false positives
Image Recognition
• CNNs (VGG16, ResNet, MobileNet)
• Facial landmarks, EAR, PERCLOS
• Thermal imaging for temperature
• Drowsiness + intoxication cues
• Strength: Non-contact, rich features
• Limitation: Lighting & occlusion
Iris Recognition
• Blink rate, eye closure, pupil
• MobileNet-V2 / ResNet-50V2
• Transfer learning for small data
• Up to 97% drowsiness accuracy
• Strength: High precision eye cues
• Limitation: Individual variation

## Slide 7
IN-VEHICLE TECHNIQUES
Biological Sensors, Behavior & Audio
Non-Invasive Biological
• Heart rate, SpO2, respiration
• rPPG from facial video
• Nasal skin temperature + EEG
• Seat-embedded sensors
• DetectDUI: vital + coordination
• Accuracy often >95%
Driving Behavior
• HMM + RNN hybrid (98%)
• Steering, speed, lane position
• Smartphone accel + LSTM/RF
• Anomaly detection (iForest)
• CART for BAC classification
• Sensitive to road conditions
Audio-Based
• ADLAIA: 12-sec speech clips
• MFCC + CNN (up to 96%)
• Pitch, rate, prosody changes
• German Alcohol Language Corpus
• Non-invasive & remote potential
• Noise & language variability

## Slide 8
OUT-VEHICLE TECHNIQUES
External Monitoring for Large-Scale Safety
Driving Behavior Analysis
▸ UAV / drone trajectory capture (highD dataset)
▸ Transmissibility algorithms on velocity
▸ CNN-LSTM on acceleration + V2X sharing
▸ Roadside cameras + spatiotemporal DL
▸ YOLO / SSD / Faster R-CNN for detection
▸ Up to 98%+ accuracy in simulations & tests
▸ Focus: lane changes, weaving, aggression
Image Recognition Systems
▸ NIR cameras at windshield for phone use
▸ DPM face detection + ML classifiers
▸ Seatbelt violation detection (NIR + RGB)
▸ SSD, CNN, Fisher Vectors methods
▸ Handles glare, tint, low light better
▸ Primarily secondary behaviors today
▸ Strong potential for impairment cues

## Slide 9
CHALLENGES
Cross-Cutting Limitations
Sensing Reliability
Hardware quality, calibration, and placement heavily affect accuracy. Environmental interference common.
Environmental Robustness
Lighting, occlusion, noise, temperature, and weather degrade performance across modalities.
Privacy & Acceptance
In-cabin biometrics raise intrusion concerns. Out-vehicle cameras raise consent and regulatory issues.
Low-Level Impairment
Subtle BAC changes are hard to distinguish from normal variability. Systems struggle below legal limits.
Data & Benchmarks
Lack of standardized datasets, statistical validation, and shared protocols limits comparison.
Deployment Feasibility
Cost, infrastructure, user compliance, and regional regulations constrain large-scale adoption.

## Slide 10
FUTURE DIRECTIONS
Four Strategic Research Paths
01
Multimodal Fusion
Combine in-vehicle physiological, behavioral, and audio signals with out-vehicle visual and trajectory data for higher robustness and lower false positives.
02
Low-Impairment Sensitivity
Develop algorithms capable of detecting subtle intoxication below legal BAC limits, where current systems often fail yet risk remains significant.
03
Scalable Deployment
Create lightweight, real-time models suitable for edge devices in vehicles and roadside units, balancing accuracy with computational cost.
04
Benchmarking & Standards
Establish common datasets, evaluation protocols, and performance metrics to enable fair comparison and accelerate reproducible research.

## Slide 11
CONCLUSION
Key Takeaways
In-vehicle systems
Have advanced rapidly with multimodal sensing but remain limited by sensor reliability, environment, and driver compliance.
Out-vehicle systems
Offer scalable, less intrusive monitoring of vehicle behavior and facial cues, yet remain underexplored for pure impairment detection.
Hybrid frameworks
Combining both paradigms can deliver comprehensive, proactive detection that neither approach achieves alone.
Road ahead
Multimodal fusion, better low-BAC sensitivity, edge-efficient models, and shared benchmarks are essential next steps.

## Slide 12
Thank You
Questions & Discussion
Source: Alsulieman, R. et al. (2026). AI-Based Approaches for Drunk Driving Detection for Traffic Safety.
IEEE Open Journal of the Computer Society, Vol. 7.